# M01-1: Project Data
## Things you need for this project work
- R — the interpreter can be installed on any operation system. For Linux, you should use the r-cran packages supplied for your Linux distribution. If you use Ubuntu, this is one of many starting points. If you use Windows, you could install R from the official CRAN web page.
- R Studio — we recommend to use R Studio for (interactive) programming with R. You can download R Studio from the official web page.
Furthermore, those of you who analyze the possible connection between terrain characteristics and land cover will inevitably require a digital elevation model (DEM). Here, possible candidates originate from (but are not limited to)
- the Shuttle Radar Topography Missing (SRTM) and
- the Advanced Spaceborne Thermal Emission and Reflection Radiometer (ASTER).
Both missions provide DEMs that come at a spatial resolution of approximately 30 m, which should be totally sufficient for our purposes. In order to get a hold of the corresponding raster images, either use
library(geodata)
elevation_30s(country = "CVP") # this will download elevation data in 90m resolution for Cabo Verde